## Slide 1: Introduction to Web and Distributed Programming

## Slide 2: Objectives
Define what is distributed computing and understand the associated opportunities and challenges that are involved
Explore the workings of the Internet and the World Wide Web
Understand the security problems involved in Web applications
Outline key technologies in web programming

## Slide 3: Overview of Distributed Systems

## Slide 4: Why Distributed/Web Computing?
World is filled with computing machines
Why not choose a single machine?
  Data separation: need to communicate
  Performance/Scaling: single machine not fast enough
  Cost-effectiveness: increasing processing power of single machine is hard and expensive
  Reliability: single machine means single point of failure

## Slide 5: Distributed System Definition
A distributed computing system is an
Autonomous set of nodes
Linked together by a computer network
Communicating by passing messages

## Slide 6: Properties of Distributed Systems
Major properties of distributed systems:
Unknown structure:
  How many machines?
  Connectivity (network topology)
Each node has a limited view of data
Fault-tolerant

## Slide 7: Distributed Systems Examples
Some examples:
Internet – World Wide Web
Cloud computing platforms (Microsoft Azure, Amazon Web Services, etc.)
Computing clusters for scientific applications
Telematics based agricultural applications (JDLink)

## Slide 8: Issues in Distributed Systems
Distributed computing introduces additional complications/issues:
Heterogeneity
  different types of hardware, software, protocols
Openness
  every service should be equally accessible to every client
Communication
  latency
  synchronization

## Slide 9: Issues in Distributed Systems
Partial Failures
  need to maintain availability and be fault-tolerant
Security
  confidentiality, integrity, availability, nonrepudiation
Scalability
  need to possibly support large number of nodes
Transparency
  system should appear to be a single system
Notes: Also Legalities, Privacy, and Data Ownership can be a challenge

## Slide 10: Communication Architectures
Client / Server
  One machine (the server) is a distinguished node
  All other machines (the clients) communicate with the server
Peer-to-Peer
  All machines can act as both client and server

## Slide 11: The Internet

## Slide 12: The Internet (History)
The Internet has roots in a Department of Defense project
  Needed a robust network that will withstand attacks
  Led to creation of ARPAnet (1960s)
  First node: UCLA – 1969
Led to other projects:
  BITnet, Csnet (1970s, 1980s): email, file transfer

## Slide 13: The Internet (History cont.)
Later, led to NSFnet (1986)
  Originally connected 5 supercomputer centers
  Used a three-tiered network architecture
  1990 – replaced ARPAnet for non-military uses
  Became available for all to use
  Eventually became the known as the Internet

## Slide 14: The Internet
The Internet is a network of networks
Based on the idea of packet switching:
  Data is divided into packets
  Packets are uniquely numbered in sequence
  Destination address is included in every packet
  Each packet may take a different route from source to destination (decided by routers)
  Packets are reassembled using sequence numbers

## Slide 15: Packet Switching Example

## Slide 16: Packet Switching
Advantages of packet switching:
  No centralized control (robust): can reroute around failed nodes
  Efficient: packets can be routed along most efficient path
  Lower cost compared to dedicated lines (circuits)

## Slide 17: Internet Protocols
Mechanism for implementing the Internet:
TCP/IP protocol(s)
Protocol: set of rules
TCP/IP Protocols
  4 layers: application, transport, internet, and link
  Each layer hides the implementation of the bottom layer

## Slide 18: TCP/IP
Application Layer Protocols - Top Layer
  Describes format of data for specific applications
  HTTP (WWW), Telnet, email, FTP (file transfer)
Transport Layer Protocols
  Describe how data is sent from end-to-end
  Handles connections, flow control, congestion
  TCP, UDP
Internet Layer Protocols
  Provides an addressing scheme
  Implements routing algorithms for transporting data to destination address
  IPv4, IPv6
Link Layer Protocols - Bottom Layer
  How two machines are physically connected
  Wired (Ethernet), Wireless (WiFi), PPP, Fiber

## Slide 19: TCP/IP - Example

## Slide 20: Internet - Addressing
Packets need to know their destination
In the Internet, each node has a designated (IP) address
Internet Protocol (IP) Addressing
  Each node has a unique address (number)
  IPv4: 32-bit binary number, IPv6: 128-bit
  e.g. 157.23.43.101
  Organizations are assigned a group of IPs

## Slide 21: Domain Names*
IP addresses (numbers) are difficult to remember
Solution: Domain Name System (DNS)
  Servers that look-up a number given an easier to remember name
  provides functionality similar to a phone book
  converts fully qualified domain names to IP addresses
Fully qualified domain name: host name and all of the domain names
Form: host-name.domain-names
  First domain is the smallest; last is the largest
  Last domain specifies the type of organization
  Example: cs.lewisu.edu
Notes: Share Bob Parsons DNS / GoDaddy learning moment.

## Slide 22: Domain Names
The last part of a domain name, called a top-level domain (TLD), indicates the type of organization:
Suffix | Organization Type/Country
edu | Educational institution
com | Commercial entity
org | Non-profit organization
net | Network-based organization
uk | United Kingdom
au | Australia
ca | Canada

## Slide 23: The World Wide Web

## Slide 24: The World Wide Web
Origins
  Tim Berners-Lee at CERN proposed the Web in 1989
  Purpose: to allow scientists to have access to many databases of scientific work through their own computers
The World Wide Web is a system of interlinked hypertext documents accessed via the Internet
  Collection of servers
  Client/server architecture
WWW is not the same as the Internet

## Slide 25: Web Browsers
A browser is a program which accesses and presents information
  text, graphics, video, sound, audio, executable programs
Mosaic - NCSA (Univ. of Illinois), in early 1993
  First to use a GUI, led to explosion of Web use
  Initially for X-Windows, under UNIX, but was ported to other platforms by late 1993
Browsers request documents from Web Servers

## Slide 26: Web Browsers (cont.)
Browsers are clients - always initiate,
Servers react
(although sometimes servers require responses)
Most requests are for existing documents, using HyperText Transfer Protocol (HTTP)
(but some requests are for program execution, with the output being returned as a document)

## Slide 27: Web Servers
Web servers provide responses to browser requests
Either existing documents or dynamically built documents
Browser-server connection is now maintained through more than one request-response cycle

## Slide 28: Web Servers (continued)
Communications between browsers and servers use HTTP
Web servers run as background processes in the operating system
  Monitor a communications port on the host, accepting HTTP messages when they appear
Web servers have two main directories:
  Document root (servable documents)
  Server root (server system software)
Document root is accessed indirectly by clients
  Its actual location is set by the server configuration file
  Requests are mapped to the actual location

## Slide 29: Common Web Servers
Apache (open source, fast, reliable)
  Currently the most popular web server
  Open source
  Cross-platform: UNIX, Linux, Mac OS X, Windows, etc.
  Installed on the computer science web server
  Maintained by editing its configuration file
IIS (Microsoft)
  Maintained through a program with a GUI interface

## Slide 30: URLs
Web addresses are URL - Uniform Resource Locator
  A server address and a path to a particular file
Example: http://www.lewisu.edu/academics/colleges.htm
Web servers return the specified file
If no file is specified, web server looks for default filename -usually index.html

## Slide 31: The HyperText Transfer Protocol
HTTP is the protocol used by ALL Web communications
Consists of two phases
  Request Phase
  Response Phase
Each communication (request or response) has two parts
  Header
  Body

## Slide 32: HTTP - Request Phase
Form:
  HTTP method domain part of URL HTTP ver.
  Header fields
  blank line
  Message body
An example of the first line of a request: GET /cs.uccp.edu/degrees.html HTTP/1.1
Most commonly used methods:
  GET - Fetch a document
  POST - Execute the document, using the data in body
  HEAD - Fetch just the header of the document
  PUT - Store a new document on the server
  DELETE - Remove a document from the server

## Slide 33: HTTP - Header Fields
Four categories of header fields
  General
  Request
  Response
  Entity
Common request fields:
  Accept: text/plain
  Accept: text/*
  If-Modified_since: date
Common response fields:
  Content-length: 488
  Content-type: text/html

## Slide 34: Multipurpose Internet Mail Extensions (MIME)
Within some fields of the form, there are specified types
  e.g.:
  Content-type: text/html
  Accept: text/plain
These are examples of Multipurpose Internet Mail Extensions (MIME)
  Originally developed for email
  Used to specify to the browser the form of a file returned by the server (attached by the server to the beginning of the document)
  Form: type/subtype
  Examples: text/plain, text/html, image/gif, image/jpeg
Server gets type from the requested file name’s suffix
  .html implies text/html
  Browser gets the type explicitly from the server

## Slide 35: HTTP - Response Phase
Form:
  Status line
  Response header fields
  blank line
  Response body
Status line format:
HTTP version status code explanation
  Example: HTTP/1.1 200 OK (version is 1.1, status code is 200, explanation - “OK”)

## Slide 36: Response Phase (cont.)
Status code is a three-digit number
First digit specifies the general status:
  1 => Informational
  2 => Success
  3 => Redirection
  4 => Client error
  5 => Server error
The header field, Content-type, is required

## Slide 37: Response Phase (cont.)
An example of a complete response header:
  HTTP/1.1 200 OK
  Date: Sat, 25 July 2009 20:15:11 GMT
  Server: Apache /2.2.3 (CentOS)
  Last-modified: Tues, 18 May 2004 16:38:38 GMT
  Etag: "1b48098-16a-3dab592dc9f80"
  Accept-ranges: bytes
  Content-length: 364
  Connection: close
  Content-type: text/html, charset=UTF-8
Both request headers and response headers must be followed by a blank line

## Slide 38: Communicate w/o Browser
Now, knowing how the HTTP protocol works, you can communicate with the web server without a browser
Just use the telnet tool (try it!):
> telnet www.lewisu.edu http
GET /index.html HTTP/1.1
Host: www.lewisu.edu
Connection: close

## Slide 39: Security Issues

## Slide 40: Security
There are many kinds of security problems with the Internet and the Web
One fundamental problem:
Getting data between a browser and a server without it being intercepted or corrupted in the process

## Slide 41: Security
There are 4 general security problems for a communication between a browser and a server:
Confidentiality (privacy): message contents should not be visible to unwanted parties
Integrity: message contents should remain unchanged during transmission
Authentication: messages should be sent to the appropriate (i.e. authorized) party
Nonrepudiation: legally prove message was sent and received

## Slide 42: Security
The basic tool to support privacy and integrity is encryption
Encryption: changing a message in such a way that only an authorized party can read it
Decrypting the message requires the knowledge of the cipher used and the key

## Slide 43: Security
Example of a simple cipher (called the Caesar cipher):
shift each letter by X positions in the alphabet
X is the key (e.g. 13)
Example of encrypting “HELLO”:

## Slide 44: Security
Many encryption algorithms use symmetric-key ciphers: same key for encryption and decryption
Problem: If the sender and the receiver both use the same key, the key must be transmitted from the sender to the receiver
Solution: Public-key encryption
  Use a public/private key pair
  It works because it is virtually impossible to compute the private key from a given public key

## Slide 45: Public-Key Encryption
Assume Bob wants to send a message to Alice
Alice uses a pair of keys (KE,KD) and
  makes key KE public
  keeps key KD private
Anyone can use the public key KE to encrypt a plaintext into a ciphertext sent to Alice
Only Alice can decrypt the ciphertext using the private key KD
ciphertext
encrypt
decrypt
plaintext
plaintext
public key
private key

## Slide 46: RSA Algorithm
The most popular encryption scheme is RSA, named after its inventors Rivest, Shamir, and Adleman (1978)
  (The RSA patent expired in 2000)
The security of the RSA cryptosystem is based on the widely believed difficulty of factoring large numbers
The best known factoring algorithm (general number field sieve) takes time exponential in the number of bits of the number to be factored

## Slide 47: Other security problems
Destruction of data on computers connected to the Internet
  Viruses and worms
  Other forms of malware
Denial-of-Service Attacks (DoS)
  Created by flooding a Web server with requests
  Even more powerful: Distributed DoS

## Slide 48: Web Development Technologies

## Slide 49: The Web Programmer’s Toolbox
Client Side
  HTML
  XML
  JavaScript
  Flash
Server Side
  PHP
  Ajax
  Servlets and JavaServer Pages
  ASP.NET
  Ruby
  Rails

## Slide 50: HTML
HTML is used to describe the general form and layout of documents
An HTML document is a mix of content and controls
Controls are tags and their attributes
  Tags often delimit content and specify something about how the content should be arranged in the document
  Attributes provide additional information about the content of a tag
Tools for creating HTML documents
  HTML editors - make document creation easier (Aptana Studio)
    (shortcuts to typing tag names, spell-checker, etc.)
  WYSIWYG HTML editors (Word)
    (need not know HTML to create HTML documents)

## Slide 51: XML
XML is a meta-markup language
XML is used to create a new markup language for a particular purpose or area
(since the tags are designed for a specific area, they can be meaningful)
No presentation details
A simple and universal way of representing and transmitting data of any textual kind

## Slide 52: JavaScript
JavaScript is a client-side, HTML-embedded, scripting language
Provides a way to access elements of HTML documents and dynamically change them
Only related to Java through syntax
Dynamically typed and not object-oriented

## Slide 53: Flash
Flash is a system for building and displaying text, graphics, sound, interactivity, and animation
Two parts:
  Authoring environment
  Player
Supports both motion and shape animation
Interactivity is supported with ActionScript
Obsolete!

## Slide 54: PHP
PHP is a server-side scripting language
Similar to JavaScript, but designed to work on the web server
Great for form processing and database access through the Web

## Slide 55: Ajax
Ajax is Asynchronous JavaScript + XML
  No new technologies or languages
Much faster for Web applications that have extensive user/server interactions
Uses asynchronous requests to the server
  Requests and receives small parts of documents, resulting in much faster responses

## Slide 56: Java Web Software
Servlets – server-side Java classes
JavaServer Pages (JSP) – a Java-based approach to server-side scripting
  An alternative to servlets
JavaServer Faces – adds an event-driven interface model on JSP

## Slide 57: Active Server Pages
ASP does what JSP and JSF do
  But in the .NET environment
Allows any .NET language to be used as a server-side scripting language
ASP.NET documents are compiled into classes

## Slide 58: Ruby
Ruby is a pure object-oriented interpreted scripting language
  Every data value is an object, and all operations are via method calls
Most operators can be redefined by the user
Both classes and objects are dynamic
Variables are all type-less references to objects

## Slide 59: Rails
Rails is a development framework for Web-based applications
Particularly useful for Web applications that access databases
Written in Ruby and uses Ruby as its primary user language
Based on the Model-View-Controller architecture

## Slide 60: Three-tier Architecture
So far we talked about client and server sides
However, modern web pages separate functionality among three tiers:
  Client tier: Web browser
  Business logic tier: Web server
  Data/Information tier: Database
Examples of database systems:
  MySQL
  SQL Server

## Slide 61: Summary
Distributed systems are used for performance, cost-effectiveness, reliability, and when data is separated
The Internet with the World Wide Web is the most famous distributed system
The Internet is based on the idea of packet switching and uses the TCP/IP protocol suite
The World Wide Web is based on the client/server architecture and uses the HTTP protocol
The four security issues (confidentiality, integrity, authentication, and nonrepudiation) can all be addressed using encryption
Common web development technologies include HTML, JavaScript (client side), PHP (server side), and MySQL (database)